## Slide 1: Chapter Six
Wide Area Network (WAN)

## Slide 2: A Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information.

## Slide 3: Introduction to WAN
utilize protocols at levels 1-3 of the OSI reference model that are optimized, both physically and logically, for extended travel
when you select a WAN technology, you will be faced with many confusing options:
  the amount of data they can deliver,
  the speed at which they operate,
  their initial and recurring costs,
  their management requirements, and
  their flexibility to include new locations or new technologies such as voice or video

## Slide 4: Switching
involves moving something through a series of intermediate steps, or segments, rather than moving it directly from start point to end point
serves the same purpose as the direct connection, but it uses transmission resources more efficiently
WAN uses switching
There are different kinds of switching:
  Circuit switching
  Packet switching
  Message switching
WANs rely primarily on packet switching, but they also make use of circuit switching, message switching,
  the relatively recent, high-speed packet-switching technology known as cell relay

## Slide 5
Circuit Switching
  involves creating a direct physical connection between sender and receiver
  a connection lasts as long as the two parties need to communicate
  allows for a fixed (and rapid) rate of transmission
  switching is done at the physical layer
  The primary drawback is
    any unused bandwidth remains exactly unused
  The most common form of circuit switching - the telephone system
  but circuit switching is also used in some networks

## Slide 6
    Advantages:
      fixed delays
      guaranteed continuous delivery
    Disadvantages
      the long connection delay (between the end of dialing and the start of ringing)
      circuits are not used when session is idle
      inefficient for bursty traffic
      usually done using a fixed rate stream (e.g., 64 Kbps) - difficult to support variable data rates

## Slide 7
2. Message Switching
  does not involve a direct physical connection
  When a network relies on message switching, the sender can fire off a transmission—after addressing it appropriately—whenever it wants
  when the sender has a block of data to be sent,
    it is stored in the first switching office (i.e., router) and then forwarded later;
    each block is received in its entirety, inspected for errors, and then transmitted - a store-and-forward network

## Slide 8
  the intermediaries aren't required to forward messages immediately.
    Instead, they can hold messages before sending them on to their next destination
  no limit on block size; routers need disk buffers
  a single block may tie up the line
  not in use anymore

## Slide 9
3. Packet Switching
  similar to message switching,
    but with a tighter limit on block size so that packets can be buffered in memory rather than on disk
  suitable for interactive traffic; no monopoly
  all transmissions are broken into units called packets,
  each of which contains addressing information that identifies both the source and destination nodes
  These packets are then routed through various intermediaries, known as Packet Switching Exchanges (PSEs)
  packet-switched networks transfer data over variable routes
  At each node the entire packet is received, stored, and then forwarded (Store-and-Forward Networks)

## Slide 10
  There has to be some kind of connection — either connectionless or connection-oriented services, depending on the type of packet-switching network involved
  In establishing the link between sender and recipient, a connection-oriented service can make use of
    either Switched Virtual Circuits (SVCs)
    or Permanent Virtual Circuits (PVCs)
  Using a switched virtual circuit is comparable to calling someone on the telephone
  Using a permanent virtual circuit, on the other hand, is more like relying on a leased line

## Slide 11
  A packet-switching network might be, for example,
    a frame relay network
    an ATM (Asynchronous Transfer Mode) network
    Etc.
  Advantage
    Line efficiency
      Single node to node link can be shared by many packets over time
      Packets queued and transmitted as fast as possible
    Data rate conversion
      Each station connects to the local node at its own speed
      Nodes buffer data if required to equalize rates
    Packets are accepted even when network is busy
      Delivery may slow down
    Priorities can be used

## Slide 12
  two popular approaches to packet switching: the Datagram Approach and the Virtual Circuit approach
    Virtual Circuit approach - a data link layer technology
      Hybrid of circuit switching and packet switching
      a single route is established between sender and receiver at the beginning of the session by sending a set-up packet
      as the packet travels all the way, the routers on the path record an entry in their internal tables and make reservation of resources at the beginning
      a call teardown deletes
      no routing decision is made by every switch for every packet; it is made only once and the virtual circuit
      used for connection-oriented services
    e.g., ATM (Asynchronous Transfer Mode)

## Slide 13
    Datagram Approach - mostly used in the network layer
      each packet is treated independently of all others
      packet in this approach is referred to as datagram
      used for connectionless services
      route chosen on packet-by-packet basis
      different packets may follow different routes
      packets may arrive out of order at the destination
      Up to receiver to re-order packets and recover from missing packets
        e.g., IP - The Internet Protocol

## Slide 15: Frame Relay
Often referred to as a fast packet switching technology
transfers variable-length packets
  up to 4 KB in size at 56 Kbps or T1 (1.544 or 2 Mbps) speeds over permanent virtual circuits
Operating only at the data link layer
was designed to take advantage of newer digital transmission capabilities, such as fiber optic cable and ISDN
These offer reliability and lowered error rates
include a means of detecting corrupted transmissions through a cyclic redundancy check, or CRC
does not include any facilities for error correction
the sender does not overwhelm the recipient with too much data

## Slide 16
because it operates over permanent virtual circuits (PVCs)
  transmissions follow a known path
  and there is no need for the transmitting devices to figure out which route is best to use at a particular time
It provides end-to-end service over a known — and fast —digital communications route
It is based on multiplexing a number of (virtual) circuits on a single communications line

## Slide 17
response to congestion
  First, to request the sending application to slow down a little its transmission speed
  Second, involves discarding frames flagged as lower-priority deliveries
Frame relay networks connecting LANs to a WAN rely on routers and switching equipment capable of providing appropriate frame-relay interfaces

## Slide 18: ATM (Asynchronous Transfer Mode)
is a transport method
capable of delivering not only data but also voice and video simultaneously and over the same communications lines
is a connection-oriented networking technology
closely tied to the ITU's recommendation on broadband ISDN (BISDN)
is good for high-speed LAN and WAN networking over a range of media types
  from the traditional coaxial cable, twisted pair, and fiber optic to communications services of the future, including FDDI, and SONET

## Slide 19
like frame relay, it is based on packet switching
  however, it relies on cell relay, a high-speed transmission method
based on fixed-size units (tiny ones only 53 bytes long) that are known as cells and that are multiplexed onto the carrier.
It is so fast as uniformly sized cells travel faster and can be routed faster
Transmission speeds are commonly 56 Kbps to 1.544 Mbps,
  but the ITU has also defined ATM speeds as high as 622 Mbps (over fiber optic cable)
ATM cell

## Slide 20
It is a wonderful means of transmitting all kinds of information at high speed.
It is reliable, flexible, scalable, and fast because it relies on higher-level protocols for error checking and correction
It can interface with both narrowband and broadband networks,
It is especially suitable for use in a network backbone

## Slide 21
  Downside
    ATM networks must be made up of ATM-compatible devices
    they are both expensive and not yet widely available
    there is a chicken-or-egg dilemma facing serious ATM deployment:
      businesses are not likely to incur the expense of investing in ATM-capable equipment if ATM services are not readily available through communications carriers over a wide area, yet carriers are reluctant to invest in ATM networking solutions if there is not enough demand for the service

## Slide 22: BISDN
is next-generation ISDN,
Is a technology that can deliver all kinds of information over the network
information is divided into two basic categories, interactive services and distributed (or distribution) services.
  Interactive services include you-and-me types of transactions, such as videoconferencing, messaging, and information retrieval
  Distributed services include you-to-me types of information that are either delivered or broadcast to the recipient
  These services are further divided into
    those that the recipient controls (for example, e-mail, video telephony, and telex) and
    those that the recipient cannot control other than by refusing to "tune in" (for example, audio and television broadcasts)

## Slide 23
The difference between narrowband ISDN and BSDN is the method of delivery
Narrowband ISDN transmissions are based on time division multiplexing (TDM),
  which uses timing as the key to interleaving multiple transmissions onto a single signal
BISDN uses ATM, with its packet switching and its little 53-byte cells
BISDN is comparable to a catalog shopping service that delivers everything from food to clothing, and ATM is like the boxes in which those products are packaged and delivered

## Slide 24
making a decision and choosing one route whenever there are multiple routes based on some criteria
it is the job of the network layer routing protocol
at the heart of such protocol is the routing algorithm that determines the path for a packet
The routing algorithm is responsible for deciding which output line an incoming packet should be transmitted on.
Routing involves two basic activities:
  determining optimal routing paths and
  transporting information groups (typically called packets) through an internetwork.
Routing and Routing Protocols

## Slide 25
If the subnet uses datagram internally this decision must be made anew for every arriving packet.
On the other hand if the subnet uses Virtual Circuits (VCs), this decision is made only when a new virtual circuit is set up.
Desirable properties of a routing algorithm:
  correctness,
  simplicity,
  robustness,
  stability,
  fairness, and
  Optimality

## Slide 26
  routing requires a host or a router to have a routing table which is constructed by the routing algorithm
  given big internetworks such as the Internet, the number of entries in the routing table becomes large and table look ups become inefficient;

## Slide 27
methods for reducing its size required
  Next-Hop Routing
    the routing table holds only the information that leads to the next hop
    Network Specific Routing
      instead of having an entry for every host connected to the same physical network, there is only one entry to define the address of the network itself

## Slide 28
Routing Vs Forwarding
  Forwarding deals with getting a packet in one line and putting it in an outgoing line.
    As a function it is the force that gets packets moving in a network.
  Routing deals with choosing the correct outgoing line to place a packet for transmission.
routing algorithms must converge rapidly.
  Convergence is the process of agreement, by all routers, on optimal routes
Routing algorithms that converge slowly can cause routing loops or network outages

## Slide 29
Types of Routing Algorithms (routing tables):
  non-adaptive (static)
  adaptive (dynamic)
    Nonadaptive (Static)
      routing decisions are not based on measurements or estimates of the current topology or traffic
      the choice of a root is computed in advance, off-line, and downloaded to the routers when the network is booted or
      an administrator enters the route for each destination into the table;
      not automatically updated when there is a change;
      may be used in a small internet, but not for big internet like the Internet

## Slide 30
    Adaptive (Dynamic)
      routing decisions are made periodically (every  sec) to reflect
        changes in the topology,
        changes in traffic,
        a shutdown of a router,
        a break in the link,
        a better route has been created, ...

## Slide 31
  Routing Protocols
    use metrics to evaluate what path will be the best for a packet to travel
    a metric is a cost assigned for passing through a network
    the cost could be
      the level of congestion of a link (mean queue length, transmission delay, average traffic),
      bandwidth,
      the geographic distance traversed by the link,
      number of hops,
      estimated transit time,
      communication cost, ...

## Slide 32
    cost may change with time
    which cost to choose depends on the application
    the total metric of a particular route is equal to the sum of the metrics of networks that comprise the route
    a router chooses the route with the shortest (smallest) metric
  Interior and Exterior Routing (protocols)
      since an internet can be large, one routing protocol cannot handle the task of updating the routing tables of all routers
      hence, an internet is divided into Autonomous Systems
      an Autonomous System (AS) is a group of networks and routers under the authority of a single administration
      routing inside an autonomous system is referred to as Interior Routing;

## Slide 33
      each AS can choose its own routing protocol
      routing between autonomous systems is referred to as Exterior Routing;
      one protocol is usually chosen to handle routing between autonomous systems;
      usually used for routing in the Internet

## Slide 34
  R1, R2, R3, and R4 use both interior and exterior routing protocols
  the rest use only interior routing protocols
  solid lines - communication between routers
  broken lines - communication between the routers that use an exterior routing protocol
    why an exterior routing protocol apart from size of an internet? - politics
      political - I hate country X hence I will not handle its traffic
      security - my information is confidential and should not pass through a hostile country

## Slide 35
      economic
        it should not pass through a competitor’s network
        I am not paid for it and hence don’t want to carry a transit packet
    such policies are typically manually configured into each router and are not part of the protocol itself

## Slide 36
    The Optimality Principle: the optimal route
      if router J is on the optimal path from I to K, then the optimal path from J to K also falls along the same route
      why?
        if a route better than R2 existed from J to K, then the route from I to K could be improved by concatenating it with R1
      the consequence of the optimality principle is that
        “the set of optimal routes from all sources to a given destination form a tree rooted at the destination”
      such a tree is called a Sink Tree

## Slide 37
  the sink tree is not necessarily unique;
  as a tree it does not contain any loops;
  each packet will be delivered within a finite and bounded number of hops; at least in theory
a subnet sink tree for router B
(distance metric is the number of hops)

## Slide 38
      the goal of a routing algorithm is to discover the sink trees for all routers
      the optimality principle and the sink tree serve as benchmarks to measure routing algorithms
    Shortest Path Routing (static) for unicast routing (by Dijkstra)
        aim:
          build a graph of the subnet - each node of the graph representing a router and each arc representing a link;
          the arcs are labeled as a function of any one of the metrics discussed (distance, hop count, ...)
        to select a route between two routers, the algorithm finds the “shortest” path between them on the graph

## Slide 39
  how does the algorithm work to find the shortest path?
      each node is labeled with its distance from the source;
      initially labeled  since no path is known
      a label may be tentative or permanent (when the shortest possible path is found - filled-in circle)

## Slide 40
  we want to find the path from A to D
  the shortest path is ABEFHD