## Slide 1: DIGITAL LOGIC CIRCUITS
Chapter One
Introduction

## Slide 2: 1.1 Digital Computer
Binary
  Two discrete values
    True 1 3.0 volts
    False 0 0.5 volts
  Very reliable
Hardware
  Electronic components
  Electromechanical devices
Software
  Instructions and data manipulated by hardware

## Slide 3: Hardware
Central Processing Unit (CPU)
  Arithmetic and Logic unit (ALU)
  Registers – holding data
  Fetch and execute control circuits
Random Access Memory (RAM)
Input Output Processor (IOP)
  Transfer data between computer and outside world
    Input, output, and input/output (I/O) devices
RAM
CPU
IOP
Output Devices
Input Devices

## Slide 4: Definitions
Computer hardware can be seen from three different points of view depending on the interest of the investigator: computer organization, computer design and computer architecture
Computer architecture (conceptual view)
  Describes major components of the computer
  User perspective of computer structure and behavior
  Architectural design deals with component specs (e.g. Processor speed, memory capacity) and combining them to build a computer
  Eg. 1. Instruction sets, addressing techniques.
  Eg. 2. Is there a multiply instruction.

## Slide 5: Definitions …
Computer organization
  Describes how the computer works
  How hardware components operate and the way they are connected together to form the computer system
    Eg. 1. Control signals
    Eg.2. Is there a hardware multiply unit or is it done by repeated addition
Computer design (computer implementation)
  Describes how the computer is built
  Once the computer specifications are formulated this step is performed
  Determines which hardware should be used and how parts are connected
    E.g. Choosing the ECL (emitter-coupled logic) circuit family for supercomputers over other types such as TTL (transistor-transistor logic)

## Slide 6: 1.2 Logic Gates
Functions of Gates can be described by
- Truth Table
- Boolean Function
- Karnaugh Map(k-Map)
Logic Gates
Gate
.
.
.
Binary
Digital
Input
Signals
Binary
Digital
Output
Signal

## Slide 7: COMBINATIONAL GATES
A
X X = (A + B)’
B
Name Symbol Function Truth Table
Logic Gates
AND
A X = A • B
X or
B X = AB
0 0 0
0 1 0
1 0 0
1 1 1
0 0 0
0 1 1
1 0 1
1 1 1
OR
A
X X = A + B
B
Inverter or I
A X X = A’
0 1
1 0
Buffer A X X = A
A X
0 0
1 1
NAND
A
X X = (AB)’
B
0 0 1
0 1 1
1 0 1
1 1 0
NOR
0 0 1
0 1 0
1 0 0
1 1 0
XOR
Exclusive OR
A X = A  B
X or
B X = A’B + AB’
0 0 0
0 1 1
1 0 1
1 1 0
A X = (A  B)’
X or
B X = A’B’+ AB
0 0 1
0 1 0
1 0 0
1 1 1
XNOR
Exclusive NOR
or Equivalence
A B X
A B X
A X
A B X
A B X
A B X
A B X

## Slide 8: 1.3 BOOLEAN ALGEBRA
Boolean Algebra
* Algebra with Binary(Boolean) Variable and Logic Operations
* Boolean Algebra is useful in Analysis and Synthesis of
Digital Logic Circuits
- Input and Output signals can be
represented by Boolean Variables, and
- Function of the Digital Logic Circuits can be represented by
Logic Operations, i.e., Boolean Function(s)
- From a Boolean function, a logic diagram
can be constructed using AND, OR, and Inverter(I)
Truth Table
* The most elementary specification of the function of a Digital Logic
Circuit is the Truth Table
- It is a table that describes the Output Values for all the combinations
of the Input Values, called MINTERMS
- n input variables → 2n minterms
Boolean Algebra

## Slide 9: LOGIC CIRCUIT DESIGN
x y z F
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1
F = x + y’z
Boolean Algebra
x
y
z
F
Truth
Table
Boolean
Function
Logic
Diagram

## Slide 10: BASIC IDENTITIES OF BOOLEAN ALGEBRA
[1] x + 0 = x
[3] x + 1 = 1
[5] x + x = x
[7] x + x’ = 1
[9] x + y = y + x
[11] x + (y + z) = (x + y) + z
[13] x(y + z) = xy +xz
[15] (x + y)’ = x’y’
[17] (x’)’ = x
[2] x • 0 = 0
[4] x • 1 = x
[6] x • x = x
[8] x • X’ = 0
[10] xy = yx
[12] x(yz) = (xy)z
[14] x + yz = (x + y)(x + z)
[16] (xy)’ = x’ + y’
[15] and [16] : De Morgan’s Theorem
Usefulness of this Table
- Simplification of the Boolean function
- Derivation of equivalent Boolean functions
to obtain logic diagrams utilizing different logic gates
-- Ordinarily ANDs, ORs, and Inverters are used to build the circuit
-- But a certain different form of Boolean function may be convenient
to obtain with NANDs or NORs
→ Applications of De Morgans Theorem
x’y’ = (x + y)’ x’+ y’= (xy)’
I, AND → NOR I, OR → NAND
Boolean Algebra

## Slide 11: Gates
Two graphic symbols for NOR gate
X
Y
Z
X
Y
Z
(x+y+z)’
x’y’z’=(x+y+z)’
X
Y
Z
X
Y
Z
(xyz)’
x’+y’+z’=(xyz)’
Two graphic symbols for NAND gate
(a) OR- invert (b) invert-AND
(a) AND- invert (b) invert-OR

## Slide 12: EQUIVALENT CIRCUITS
F = ABC + ABC’ + A’C .......…… (1)
= AB(C + C’) + A’C [13] ..…. (2)
= AB • 1 + A’C [7]
= AB + A’C [4] ...…. (3)
(1)
(2)
(3)
Many different logic diagrams are possible for a given Function
Boolean Algebra
A
B
C
F
A
B
C
F
F
A
B
C

## Slide 13: Logic Gates > 2 Inputs
AND
  X=1 if and only if all inputs =1
OR
  X=1 if any input =1
Exclusive-OR
  X=1 if an odd number of inputs=1
NAND
  Complement of AND
NOR
  Complement of OR
Exclusive-NOR
  Complement of exclusive-OR
All gates except NAND/NOR/Exclusive-NOR can be constructed from 2 input gates by cascading. But this is not the case for NAND/NOR/Exclusive-NOR because of their definitions (i.e., NAND is always opposite of AND, NOR is always opposite of OR, & Exclusive- NOR is always opposite of XOR).

## Slide 14: 1.4 Map SIMPLIFICATION
Truth
Table
Boolean
Function
Unique
Many different expressions exist
Simplification from Boolean function
- Finding an equivalent expression that is least expensive to implement
- For a simple function, it is possible to obtain
a simple expression for low cost implementation
- But, with complex functions, it is a very difficult task
Karnaugh Map (K-map) is a simple procedure for
simplifying Boolean expressions.
Truth
Table
Boolean
function
Karnaugh
Map
Simplified
Boolean
Function
Map Simplification

## Slide 15: KARNAUGH MAP
Karnaugh Map for an n-input digital logic circuit (n-variable sum-of-products
form of Boolean Function, or Truth Table) is
- Rectangle divided into 2n cells
- Each cell is associated with a Minterm
- An output(function) value for each input value associated with a
minterm is written in the cell representing the minterm
→ 1-cell, 0-cell
Each Minterm is identified by a decimal number whose binary representation
is identical to the binary interpretation of the input values of the minterm.
Minterms are arranged using reflected binary code or Gray code
(named after Frank Gray).
Generating Gray codes: Reflect-and-prefix method
Purpose is to successive values differ in one bit.
This is useful for combining adjacent squares.
Adjacent squares are squares that differ by only one variable, i.e., by the complemented and uncomplemented versions of the variable. Adjacent squares are placed horizontally or vertically not diagonally.
Map Simplification

## Slide 16
x F
0 1
1 0
x
0
1
0
0
x
0
1
1
1
Karnaugh Map
value
of F
Identification
of the cell
x y F
0 0 0
0 1 1
1 0 1
1 1 1
x
y
0 1
0
1
0 1
2 3
x
y
0 1
0
1
0 1
1 1
F(x) =
F(x,y) =  (1,2,3)
1-cell
 (0)

## Slide 17: KARNAUGH MAP
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 0
1 1 0 0
1 1 1 0
0 1 0 1
1 0 0 0
0 0 0 0 0
0 0 0 1 1
0 0 1 0 0
0 0 1 1 1
0 1 0 0 0
0 1 0 1 0
0 1 1 0 1
0 1 1 1 0
1 0 0 0 1
1 0 0 1 1
1 0 1 0 0
1 0 1 1 1
1 1 0 0 0
1 1 0 1 0
1 1 1 0 1
1 1 1 1 0
x
yz
00 01 11 10
0
0 1 3 2
4 5 7 6
x
yz
00 01 11 10
0
1
F(x,y,z) =  (1,2,4)
1
x
y
z
uv
wx
00 01 11 10
00
01
11
10
0 1 3 2
4 5 7 6
12 13 15 14
8 9 11 10
uv
wx
00 01 11 10
00
01
11 0 0 0 1
10 1 1 1 0
0 1 1 0
0 0 0 1
F(u,v,w,x) =  (1,3,6,8,9,11,14)
u
v
w
x
Map Simplification
x y z F
u v w x F

## Slide 18: MAP SIMPLIFICATION - Rules-
Insert a “1” into each square that the function generates a value of 1
Form one or more rectangles by grouping together adjacent squares containing a 1
  Number of square in each rectangle must be a power of 2
  Top and bottom squares in a column are adjacent
  Left- and right-most squares in a row are adjacent
  All four corner squares are adjacent
  Minimize number of rectangles and maximize number of adjacent squares combined
  Groups of combined adjacent squares may share one or more squares with one or more groups
Map Simplification

## Slide 19: MAP SIMPLIFICATION - Rules-
F = xy’+ xy can be reduced to F = x
From the map
x
y
0 1
0
1
1 1
0 0
 (2,3)
F(x,y) =
2 adjacent cells xy’ and xy
→ merge them to a larger cell x
= xy’+ xy
= x
Map Simplification

## Slide 20: MAP SIMPLIFICATION - MORE THAN 2 CELLS -
u’v’w’x’ + u’v’w’x + u’v’wx + u’v’wx’
= u’v’w’(x’+x) + u’v’w(x+x’)
= u’v’w’ + u’v’w
= u’v’(w’+w)
= u’v’
uv
wx
1 1 1 1
1 1
1 1
uv
wx
1 1 1 1
1 1
1 1
u
v
w
x
u
v
w
x
u’v’
uw
u’x’
v’x
1 1
1 1
vw’
u’v’w’x’+u’v’w’x+u’vw’x’+u’vw’x+uvw’x’+uvw’x+uv’w’x’+uv’w’x
= u’v’w’(x’+x) + u’vw’(x’+x) + uvw’(x’+x) + uv’w’(x’+x)
= u’(v’+v)w’ + u(v’+v)w’
= (u’+u)w’ = w’
Map Simplification
u
v
w
x
uv
wx
1 1
1 1
1 1
1 1
u
v
uv
1 1
1 1
1 1
1 1
1 1 1 1
x
w’
u
V’
w

## Slide 21: MAP SIMPLIFICATION
F(u,v,w,x) =  (0,1,2,9,13,15)
F = u’v’x’ + v’w’x + uvx
Map Simplification
wx
x
uv
00 01 11 10
00
01 0 0 0 0
11 0 1 1 0
10 0 1 0 0
1 1 0 1
u
v
w
0
0
0
0
1
1
0
1
0
1
1
0
0
1
0
0

## Slide 22: IMPLEMENTATION OF K-MAPS - Sum-of-Products Form -
Logic function represented by a Karnaugh map
can be implemented in the form of I-AND-OR
A cell or a collection of the adjacent 1-cells can
be realized by an AND gate, with some inversion of the input variables.
x
y
z
x’
y’
z’
x’
y
z’
x
y
z’
1
1
1
F(x,y,z) =  (0,2,6)
1 1
1
x’
z’
y
z’
Map Simplification

x’
y
x
y
z’
x’
y’
z’
F
x
z
y
z
F
I AND OR
z’


## Slide 23: IMPLEMENTATION OF K-MAPS - Product-of-Sums Form -
Logic function represented by a Karnaugh map
can be implemented in the form of I-OR-AND
If we implement a Karnaugh map using 0-cells,
the complement of F, i.e., F’, can be obtained.
Thus, by complementing F’ using DeMorgan’s
theorem F can be obtained
F(x,y,z) = (0,2,6)
x
y
z
x
y’
z
F’ = xy’ + z
F = (xy’)’z’
= (x’ + y)z’
x
y
z
F
I OR AND
Map Simplification
0
0
1
1
0
0
0
1

## Slide 24: Alternative Implementations
NAND implementation of sum-of-products
  Eg. F(x,y,z) = (0,2,6)

F
I NAND NAND
x
z
y
z
F
I NAND NAND
x
z
y
z

## Slide 25: Alternative Implementations …
NOR implementation of product-of-sums
  Eg. F(x,y,z) = (0,2,6)
x
y
z
F
I NOR NOR
x
y
z
F
I NOR NOR

## Slide 26: IMPLEMENTATION OF K-MAPS - Don’t-Care Conditions -
In some logic circuits, the output responses
for some input conditions are don’t cares
i.e. they can be either 1 or 0.
In K-maps, don’t-care conditions are represented
by x’s in the corresponding cells.
Don’t-care conditions are useful in minimizing
the logic functions using K-map.
- Can be considered either 1 or 0
- Thus increases the chances of merging cells into the larger cells
Combine 1’s and x’s to enclose the maximum number of adjacent
squares
 Reduce the number of variables in the product terms
E.g.: F(A,B,C)=∑(0,2,6)
d(A,B,C)=∑(1,3,5)
z
x
y
1 x x 1
x 1
x’
yz’
x
y
z
F
Map Simplification

## Slide 27: 1.5 COMBINATIONAL LOGIC CIRCUITS
Cluster of logic gates with some number of inputs and outputs
Output values are determined by the binary computations performed on the input values
Can be described by
  A truth table
  A Boolean function for each output

## Slide 28: COMBINATIONAL LOGIC CIRCUITS
Half Adder
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1
cn = xy + xcn-1+ ycn-1
= xy + (x  y)cn-1
s = x’y’cn-1+x’yc’n-1+xy’c’n-1+xycn-1
= x  y  cn-1 = (x  y)  cn-1
x
y
cn-1
x
y
cn-1
cn
s
Combinational Logic Circuits
x
y
x
y
c = xy s = xy’ + x’y
= x  y
x
y
c
s
x
y
cn-1
S
cn
Full Adder
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
x y c s
0
1
0
0
0
0
1
1
x y cn-1 cn s
0
0
1
0
0
1
1
1
0
1
0
1
1
0
1
0
Q. How can you construct a full adder from two half adders?

## Slide 29: 1.6 Flip Flops
Combinational circuits vs sequential circuits (sc)
  For combinational circuits the outputs at any given time are entirely dependent on the inputs that are present at that time.
  Sequential circuits contain storage elements
  so that the output depends on previous inputs

## Slide 30: 1.6 Flip Flops
Types of SC
  Synchronous (clocked synchronous circuits)
    Most common
    All storage elements of the circuit are affected at discrete instants of time
    Achieved through a timing device called clock pulse generator
    Affected (or operated) when the clock pulse is either 1 or 0

## Slide 31: Flip Flops …
Asynchronous
  No clock to synchronize parts of the system
  This creates a number of problems and hence these are not widely used
SC use storage elements called flip-flops. Many types exist.
Flip-flop is binary cell that can hold the value of one bit
Two outputs
  Normal value
  Complement
Maintains state until next clock pulse
  We have many types of flip-flops

## Slide 32: FLIP FLOPS …
Characteristics
- 2 stable states
- Memory capability
- Operation is specified by a Characteristic Table
In order to be used in the computer circuits, the flip flop should
have input terminals and output terminals so that it can be set to a certain
state, and its state can be read externally.
R
S
Q
Q’
S R Q(t+1)
0 0 Q(t) No change
0 1 0 Clear to 0
1 0 1 Set to 1
1 1 indeterminate
(forbidden)
Flip Flops
SR-Flip Flop (Latch) (SR- Set , Reset)

## Slide 33: CLOCKED FLIP FLOPS
In a large digital system with many flip flops, operations of individual flip flops
are required to be synchronized to a clock pulse. Otherwise,
the operations of the system may be unpredictable.
R
S
Q
Q’
c
(clock)
Flip Flops
S Q
c
R Q’
operates when operates when
clock is high clock is low
S Q
c
R Q’
Clock pulse allows the flip flop to change state only
when there is a clock pulse appearing at the c terminal.
We call the above flip flop a Clocked RS Latch, and symbolically as

## Slide 34: D Flip-Flop
D-Latch
Forbidden input values are forced not to occur
by using an inverter between the inputs
Flip Flops
Q
Q’
D(data)
D Q
Q’
D Q(t+1)
0 0
1 1
Its characteristic equation is Q(t+1)=D

## Slide 35: D Flip-Flop …
What if you want to store a 1?
After D=1 D=0, next clock pulse causes Q(t+1)=0
Solution:
Disable clock or
Feed output of Q to D input
Flip Flops
Q
D Q
Q’
c

## Slide 36: FLIP FLOPS …
JK Flip-flop
T Flip-Flop
  Apply signal to toggle (switch) from one
  state to another
  Characteristic equation is
    Q(t+1)=Q(t) XOR T
T Q(t+1)
0 Q(t) No change
1 Q’(t) Complement
Flip Flops
J Q
k Q’
c
J K Q(t+1)
0 0 Q(t) No change
0 1 0 Clear to 0
1 0 1 Set to 1
1 1 Q’(t) Complement
J Q
k Q’
c
T

## Slide 37: EDGE-TRIGGERED FLIP FLOPS
Characteristics
- State transition occurs at the rising edge or
falling edge of the clock pulse
Rising edge (positive)
Falling edge (negative)
respond to the input only at this time
respond to the input only at this time
Flip Flops
S Q
c
R Q’

## Slide 38: Flip-Flop Excitation Table
What input values generate a given pair of current and next values
of Q?
  Used for the design of sequential circuits.
Flip Flops

## Slide 39: SR Flip-Flop
Flip Flops
S R Q(t+1)
0 0 Q(t)
0 1 0
1 0 1
1 1 ?
Q(t) Q(t+1) S R
0 0 0 x
0 1 1 0
1 0 0 1
1 1 x 0
Characteristic
Excitation

## Slide 40: D Flip-Flop
Flip Flops
D Q(t+1)
0 0
1
Q(t) Q(t+1) D
0 0 0
0 1 1
1 0 0
1 1 1
Characteristic
Excitation

## Slide 41: JK Flip-Flop
Flip Flops
J K Q(t+1)
0 0 Q(t)
0 1 0
1 0 1
1 1 Q’(t)
Q(t) Q(t+1) J K
0 0 0 x
0 1 1 x
1 0 x 1
1 1 x 0
Characteristic
Excitation

## Slide 42: T Flip-Flop
Flip Flops
T Q(t+1)
0 Q(t)
1 Q’(t)
Q(t) Q(t+1) T
0 0 0
0 1 1
1 0 1
1 1 0
Characteristic
Excitation

## Slide 43: 1.7 SEQUENTIAL CIRCUITS
Flip-flops and gates connected together
Combinational circuit block
  Gates only
  Input from external sources and flip-flop output
  Output goes to external destinations and flip-flops
Flip-flops
  Input from clock and combinational circuit
  Output to external destinations and combinational circuit
Flip-flop input equations are output of combinational circuits that is fed to flip-flop inputs
Flip Flops
Combinational circuit
Flip-Flops
Inputs
Output
Clock

## Slide 44: SEQUENTIAL CIRCUIT BLOCK DIAGRAM
A set of flip-flop input equations specifies a sequential circuit in algebraic form
  Equivalently, a sequential circuit is specified by: time sequence of external inputs, external outputs, and internal flip-flop states
Outputs are determined by external inputs and present state of flip-flops
State changes occur whenever clock signal arrives
State table helps in the design of sequential circuits
  It shows the state transition of flip-flops from their present states to their n-ext states given the external inputs. It also shows values for the external o-utputs
Flip Flops

## Slide 45: Example of a sequential circuit
Flip-flop input equations: DA=Ax+Bx and DB=A’X
External output: y=Ax’+Bx’
  State table for the example circuit

## Slide 46: State Diagram
State Diagram
  Same information as state table
    Different representation
  Circle is state
    Flip-flop values inside
  Line connecting circles is transition
    “Input value/ output value” for present state

## Slide 47: SEQUENTIAL CIRCUITS - DESIGN EXAMPLE
Design Problem
  Clocked sequential circuit that is a two bit binary counter
    Increment when input x is 1
    Remain unchanged when input x is 0
  Construct
    State diagram
    Excitation table
    Logic circuit diagram
  Note: Number of flip-flops needed for the circuit is equal to the number of bits listed within the circles of the state diagram
Flip Flops

## Slide 48: SEQUENTIAL CIRCUITS - DESIGN EXAMPLE …
Design Procedure:
Specification  State Diagram  State Table 
Excitation Table  Karnaugh Map  Circuit Diagram
Example: 2-bit Counter -> 2 FF's
current next
state input state FF inputs
A B x A B Ja Ka Jb Kb
0 0 0 0 0 0 d 0 d
0 0 1 0 1 0 d 1 d
0 1 0 0 1 0 d d 0
0 1 1 1 0 1 d d 1
1 0 0 1 0 d 0 0 d
1 0 1 1 1 d 0 1 d
1 1 0 1 1 d 0 d 0
1 1 1 0 0 d 1 d 1
A
B
x
Ja
1
d d
d d
x
A
B
Ka
d d
d d
1
Kb
A
B
x
1
1
d
d
d
d
Ja = Bx Ka = Bx Jb = x Kb = x
clock
00
01
10
11
x=0
x=1
x=0
x=1
x=0
x=1
x=0
x=1
Sequential Circuits
J Q
C
K Q'
J Q
C
K Q'
x
A
A
B
x
1 d
1 d
d
d
Jb
B